SC95

Spectra (XY files) visualization and manipulation

Program Overview

Abilities

- multiple-spectra input (listed in .lst file), fast figure export to .gif, .jpg, and .hpgl; animation and animated .gif generation

- automatic peak labeling

- spectral operations (average, sum, difference, addition, multiplication, absorption ( transmittance conversion, x-shift, number of points change, derivative, integral, convolution, FFT, spectral scaling and conformer analysis, polynomial baseline and spectra comparison, peak fit)

Input

- .PRN files (default), x y numbers in column, no label, no separator, same for .TXT files

- .SPC binary files, SpectraCalc format

- .PLT Biotools format, first line skipped, then three columns x y_Raman y_ROA

- .TAB files, with spectra only, if required (Options_Misc.), to draw spectral lines or to scale calculated spectra

Spectral Operations

Average , will be added as a new spectrum

Sum will be added as a new spectrum

Difference will be added as a new spectrum

Weighed difference , c is adjustable, will be added as a new spectrum

Spectrum - CONST (constant shift)

Spectrum ( CONST (multiplication, e.g. negative spectrum can be generated with CONST = -1)

Multiply intensity by frequency

Absorbance

Transmittance (%)

Shift X-scale

Resample new number of points can be defined, equidistant in current x-units

Derivative, integral spectra - added as new ones

Convolutions with Gaussian or Lorentzian functions, used e.g. for smoothing

,

N-Point Smoothing quadratic spline over N-points

FFT - make (fast) Fourier transformation

TorsionFit (obsolete option)

ConformerFit enables spectral scaling and comparison with experiment; experimental spectrum must be loaded first, in Option_Misc. the .TAB files must be selected. Simultaneous scaling of two kinds of spectra (e.g. IR and VCD) and comparison to experiment possible; then primary and secondary columns in .TAB files (Options_Misc.) must be chosen.

Polynomial Baseline Polynom of any order constructed from chosen points, subtracted from the spectrum

Two-Spectra Comparison: spectral shape similarity quantification, load two spectra (S1, S2) only, stacked mode

- (Optional) normalizes spectra

- Adjusts x-scale from selected corresponding points in the first and second spectrum,

- Makes difference spectrum and calculates its norm.

Peak Fit. Gaussian or Lorentzian peak fit of visible spectral region, conjugate gradient minimization possible.