specomp.f

Decomposes a spectrum S into subspectra {Si} (iinv>0) or just writes a deviation

Spectral list in SP.LST, the decomposed one is the first.

Mathematics

Decomposition: , i = 1…N,

We minimize  with a condition .

Option file SP.OPT:

aa	intensity scale damping

aa [10]

adapt	dynamic scale adjustment during the fit (not very successful option)

if adapt ( 0 then instead of the original spectra Si((),take Si’(() = aSi(k( - b); then a, k, and b are found by a non-linear minimization.

if adapt = 0 then a = 1, k = 1, b = 0

adapt [0]

alph	(, the bias factor, see also cav

al [0.001]

bb	x- scale shift damping

bb [4e-3]

bin 	systematic x- shift multiplier

bin [0]

cav the bias parameter, if cav = 0 then cave = 1/N else cave = cav.

cav [0]

energy if <> 0 iterative model with all positive coefficients

ienergy [0]

iinv	make the RMS decomposition

iinv [1]

ino	0-normalize A^2, 1-normalize |A|

ino [0]

icol 	collective spectra fitting

icol [0]

iraw    if iraw = 1, do a raw direct fit, without

iraw [0]

iwr 	larger output for iwr>0

iwr [0]

kin 	systematic x- scale multiplier

kin [1]

kk	x- scale multiplier damping

kk [1000]

normc  if 0, normalize all spectra

normc [0]

npar	2 or 3, number of fitting parameters

npar [3]

wmin 	lower wavenumber limit

wmin  [-10000]

wmax upper wavenumber limit

wmax  [+10000]

xscale	if xscale = 1 then scale frequency in reference spectra during input,

(’ = xs0 + xs1 ( (  + xs2 ( (2

xscale [0]

xs0

xs0 [0]

xs1

xs0 [1]

xs2

xs2 [0]

Remark-theory

We minimize  with a condition .

Figure: Dependence of the coefficients on (.

specomp3.f

2-D PES surface via the Fourier Transform Method

Input:	SPECOMP3.OPT

SMOOTH.OPT

ANGLE.LST

SP.LST    spectral list, first is reference

pes.txt PES estimate (optional)

SMOOTH.OPT

IFI   delfi

5

IPSI delpsi

5

PSII psimin

-185

PSIA psimax

185

FII  fimin

-185

FIA  fimax

185

KMAX  kmax maximum frequency

3

SPECOMP3.OPT

WMIN

200

WMAX

1800

NP

1000

ITER

10

TEMP

273

GLIM

1e-3

ELIM

1e-4

KMAX

3

NGUE	number of initial guesses

1

LWR

t

XS0

0

XS1

1

XS2

0

specomp3 will all input spectra rewrite according to WMIN,WMAX and NP!!

(2kmax+1)2 parameters

The free energy is decomposed to smooth sine and cosine functions,

, , , , , , , etc.

We define ,

A can be included in (G via g11