Options for QGRAD

(in file Q.OPT, can be changed during run)

Bour, P.; Keiderling, T. A. J. Chem. Phys. 2002, 117, 4126-4132.

Bour, P. Collect. Czech. Chem. Commun. 2005, 70, 1315-1340.

{OPTION

variable (usually logicals start with "l")}

MAXSTEP

maxstep

maximum number of optimization steps (integer)

default: -1 … goes forever

del e max

dll

tolerance for energy, if energy goes higher by dll than coordinate step is decreased

default: 0.05 au

force field

filename

file with force field, default FILE.FC

hessian update

lupdate

default: true

cartesian update

lff

Hessian update in Cartesian coordinates, default: true

gaussian input

filename

Default: G98.INP for Gaussian

new charges

lnewcharges

(miscellaneous option for optimization with charges)

dalt

ldalton

working with Dalton (files d.mol, d.dal etc)

SYMMETRY

pp

use symmetry if present, 3 character variable (default:all, possible:'c1 ', 'c2x','c2y','c2z','sxy','szx','syz')

S-TOL

tol

tolerance for symmetry determination, def:0.01

NOSYM

<no option>, switch off symmetry

allRFO

lrfo

Rational function optimization, default: true

qmax

qmax

default: 0.8, maximum step in normal coordinates

checkgrad

lchkg

def:false, check that coordinate step goes along gradient, for individual mode

checktotalgrad

lch2

def:true, check that coordinate step goes along gradient, for total gradient

coordinates

filename

def:G98.OUT, file with coordinates, for Gaussian calculations

CHARGE

lcharges

for case of Gaussian calculation with point charges

gradx

filename

def:G98.OUT, file with gradient, for Gaussian calculations

fixed range

istart iend

integers, which modes are fixed - not optimized, obsolete

modes fixed

N, n1…nN

list of fixed modes, can be also defined with interval wmin…wmax:

wmin

wmin [cm-1]

wmax

wmax [cm-1]

glimit

glim

Convergence limit for gradient norm, def: 0.0001.

s-matrix

filename

File name with s-matrix, def: F.INP

ignore zero

li0

ignore zero frequency modes, def: true

masses

filename

def: FTRY.INP, where to find atomic masses

smatout

lsout

write out S-matrix, def:false.

project

lpr

project translations and rotations, def: true

fixed

npar

ki,atom1…atomknpar, Aknpar, Bknpar

…

knpar,atom1…atomknpar, Aknpar, Bknpar

def: npar=0; number of fixed geometrical parameters, k=2..bond length, k=3…bond angle, k=4…torsion angle, A … value, B … potential barrier, fixation via energy term ~B*(A-A0)2

details: Bouř, P. Collect. Czech. Chem. Commun. 2005, 70, 1315-1340

same

nsame

i1  j1  B1

…

insame  jnsame  Bnsame

def:0; number of same parameters, B-barrier, similarly as for fixed, if i1 <0 then constant difference