Program S4: Keyword overview

Petr Bouř

Institute of Organic Chemistry and Biochemistry

Flemingovo nam.2, 166 10, Praha 6, Czech Republic

Version 1999-2008

PURPOSE

S4 program calculates anharmonic vibrational energies of molecules. Current version reads output of the Gaussian program. The older program M4 is now a part of S4 and calculates spectra; it has a separate option file M4.OPT. In the file S4.OPT options for S4 are specified. Keywords follow from the first line each on a separate line until the END keyword is reached. Single space must precede each keyword, keywords are case sensitive. In the following list control variables and default values are specified for each keyword.

ABILITIES

PT2 (classical second-order perturbational approach)

PT2 degeneracy corrected PT2 (kw:ENA2)

PT2 –big AH constants (kw: ENAS)

VSCF

PHASE

VCI

VCI+PT2 combination

vibrational averaging of NMR shifts, J-couplings, ORD, dipoles, geometry

Key steps in anharmonic calculation:

1) Prepare Gaussian input, usually 6N geometries, N= number of atoms.

The pmz script can be used.

2) Calculate higher energy or other property derivatives numerically, i.e. run Gaussian on pmz output

3) Run s4

OPTIONS

1. General options

2. Diagonalization options

1. General options (start after a blank character on each line of S4.OPT)

Input-related

L36

L36 [false]

File FILE.36.OUT used for differentiation, calculate all two-atomic quartic constants.

L37

L37 [false]

File FILE.36.OUT used for differentiation, calculate all three-atomic quartic constants.

AH4L

ah4l [0.2]

cut=off limit for the rotational part of quartic perturbation

ANSATZ  	[lans=true]

lans

The frequencies calculated from phase integrals will be used as a new basis.

ASL		[asl=2.0]

asl

Cut-off limit for the cubic and quartic force fields, if lsparse=true.

ASK		[asl=2.0]

ask

Second cut-off limit for the cubic and quartic force fields, if lsparse=true, used to divide H = H0 + H1 + H2, se DC and DC2 options

A44

a44 [0.0001]

The limit in the iterative projection of space coordinates from the quartic FF.

BLOCK  	[lblock=false]

ncan

ican(1),ican(2) ... ican(ncan)

Some states will be "frozen", ncan .. number of the blocked states, ican .. the list, counted from the lowest.

COFF

COFF (1.0)

cage dimension for plane waves

if COFF>0 ... global

COFF<0 ... local

DC      	[dc=false]

The perturbational correction will be applied to the VCI energies.

(if LENAS then Hamiltonian is partitioned, see ASL and ASK keywors, else just remaining states added).

DC2      	[dc=true]

The perturbational correction will be applied to the VCI energies including second order.

DOH 	[doh=0.0]

doh

The step of OH, otherwise OH doubles when number of states overflows. See OH, NG0.

END

Terminates the list of options.

HW      	[hw=false]

hw

The full vibrational Hamiltonian and the eigenvalues and eigenvectors will be listed in S4.OUT. For a bigger molecule very large output can be generated!

IAAA

iaaa, iopt(5) [0]

if=1, disable AH dipolar derivatives

IEXC

iexc [0]

m1 l1

.....

miexc liexc

If iexc<>0, then for selected modes m1  ..... miexc define maximal excitations l1 .....  liexc.

program numbering used (N7 ...N)

IBR

ibr [0]

restart diagonalization from symmetry block ibr

IP4

ip4 [1]

number of cycles for iterative projection of quartic ff

LCIA [false]

In setstate2 (for IEXC>0) take all states according to LEXCL, regardless to the interaction to ground end fundamentals.

LEXCL  	[lexcl=5]

lexcl

Limit for excited states (lexcl<6)

LH40

lh40 [F]

add kinetic part of quartic potential

LINEAR  	[linear=false]

This option must be indicated for a linear molecule.

LQD     	[lqd=true]

lqd

The quartic off-diagonal terms will be considered.

LQD1    	[lqd1=true]

lqd1

The quartic off-diagonal terms will be calculated only in the final

Hamiltonian.

LPC

lpc

take projected quartic

L4  	[l4=true]

l4

Quartic off-diagonals as diiij and diijk included.

VSCF

lvscf  [false]

Vibrational self-consistent field, frequency calculation

LXS

lxs

sparce ff (see xlim for cutoff)

M4

lm4

Perform the spectrum calculation (separate options M4.OPT) after the frequencies.Z

M4ONLY

lm4only

Start the spectrum calculation immediately

MODCPL

modcpl [iopt(17)=0]

Maximum number of coupled modes (no limit for zero). Works with the SPARSE option only.

MASS

nmass

iat am(iat) (1)

..

(nmass)

define non-default atomic masses

NGH

ngh [1]

cosinus basis - how many atoms are excited

NHAND  	[nhand=0]

nhand

nhand of additional states defined in the file HAND.OPT

NZF

nzf

iqf(1)..iwf(nzf)

wf(1)..wf(nzf)

nzf frequencies will be substituted, as defined

NOENA   	[lena=true]

The perturbation calculation will not be performed.

ENA2	call the perturbation calculation with the degeneracy-corrected PT2 formula

lena2 [true]

ENAS	call the perturbation calculation with the degeneracy-corrected PT2 formula, for super-sparse cubic and quartic FFs

lenas [false]

ISET

iset, iopt(2)

how many atoms can be excited (for Iset=2 .. cosinus basis)

iset=4, iexc>0 ... take states also interacting with existing states

NG0

NG0 [iopt(18)=12000]

Limit dimension of the direct diagonalization.

NOHBIG  	[lhbig=true]

The variational calculation will not be performed.

NQ1

iopt(1) 1..5

how many modes can be excited for a basis state

NZF     	[nzf=0]

nzf

iwf(1) iwf(2) ... iwf(nzf)

wf(1) wf(2) ... wf(nzf)

nzf frequencies will be substituted and used in the basis (iwf-frequency number, wf - new value)

OH       [oh=0.0]

oh

The v parameter, criterium for selection of the basis functions. See NG0, DOH.

PHASE   	[lphase=true]

lphase

The phase integrals for normal modes will be calculated.

STOL	[stol=1e-4]

stol

tolerance for S-matrix inaccuracy

QUARTIC 	[quartic=true]

The quartic corrections will be calculated. In this case, a two-point differentiation is required.

L411 [l411=false]

Quartic Cartesian constants from one atom only, D((,((,((,((.

PHASE

lphase [T]

phase integrals calculated for normal modes

RDST	[rdst=false]

Read-in states to diagonalize from STATES.LST scratch file.

RESTART 	[restart=false]

The normal mode force constants will be read from the disk files CQ.CUB and CQ.QUA, rather than calculated again from the cartesians.

SCALED  	[scaled=false]

The S-matrix will be read in from the F.INP file, rather than from C5.OUT.

SPARSE	[lsparse=false]

lsparse

Algorithm for sparse cubic and quartic fields used.

SYMMETRY

sstr

Symmetry of vibrational modes will be defined in the file SYM.OPT. sstr is a three-letter code of molecular group, capitals must be used (C2V, D2H etc. in the [1X,A3] format).

SSTEP

sstep

differentiation step, in Å

TOL3/TOL4

tol3/tol4  [0.0]

Cuttoffs for normal mode cubic/quartic constants, in cm-1 (dimensionless normal mode coordinates).

2. Diagonalization options

CONT

lcont [false]

rcont [0.1 cm-1]

set off diagonals in H to rcont, an experimental option

DT

dt [0.1 fs]

With the LFT option, integration time step

GRADCONV	[gradconv=0.0000001]

gradconv

The gradient limit of the eigen-functional, for convergence of diagonalization routine MITIN.

FTW0

w0 [0 cm-1]

Damping frequency limit, see FTNI.

FTNI

ni [0.0]

Damping frequency barrier, see also FTW0, the vector propagates approximately as exp(-i(t)exp[ - ni ((-(0)].

HSLIMIT	[HSLIMIT=0.0]

hslim

Cut off limit for Hamiltonian elements (in cm-1).

IERM

ierm [0]

restart diagonalization from EV # ierm

IMT3

imt3, iopt(4) [0]

if =1, then do not diagonalize DOHBIG2 and just grab calculated eigenvectors and eigenvalues

LVAR

lvar

vary dimension of iterative subspace in mitin

LG

lg [false]

Use Gaussian bands for convolution, for the LFT option

LFT

lft [false]

Use the direct Fourier transform based generation of the spectra

LFTG

lftg [false]

With the LFT option, use exact ground state.

LTO

lto [false]

LTOP

etlim [4000] det [400] etal [0.9]

Empirically scale the Hamiltonian diagonal elements. For Hii > etlim, Hii’ = Hii ( (etal +(1 - etal )( exp[-(Hii - etlim)2det-2]).

lto=lopt(40) , etlim=ropt(17), etal=ropt(18), det=ropt(19) For the direct diagonalization only.

MITIN  	[lmitin=false]

lmitin

nmm vmm

The Mitin's routine will be used for diagonalization, nem .. number of lowest eigenvalues to be calculated, smaller than vmm.

nmm is the dimension of iterative sub-space.

NMD

nmd  [10000]

With the LFT option, number of integration steps

NMIT   	[nmit=0]

nmit

Number of eigenvalues already computed (restart option for MITIN routine).

NP

np  [4000]

With the LFT option, number of spectral points

NWV

nww [10]

With the LFT option, number of random vectors.

OLIMIT   [olimit=0.000001]

olimit

The sub-space convergence limit for the MITIN diagonalization routine.

WMIN

wmin [0]

With the LFT option, lower range limit [cm-1]

WMAX

wmax [4000]

With the LFT option, upper range limit [cm-1]

3. Options for local oscillator basis (located on atoms)

CUT1

cut 1 [2.0 Å]

Cut off for multiple center excitations.

ICEM

icem [4]

Maximum number of excited centers

ICEX

nc (ice(i),i=1,nc) [all maximum 3*nat]

For each number of excitation maximum number of centers (e.g. if ice(6)=4,  6(excited states will be limited to those comprising 4 and less atoms).

LBTO

wlbtol [10 cm-1]

Tolerance beyond which the local mode is switched off.

LCBS

lcbs [false]

Start calculation in the local Cartesian basis.                     (( main option)

LCB2

lcb2 [true]

Include harmonic constants.

LCB3

lcb3 [false]

Include cubic constants.

LCB4

lcb4 [false]

Include quartic constants.

XDIA

lxdia [true]

Diagonalize the atomic force fields locally.

Miscellaneous

DAFAC

dafac [1.0]

Damping factor for anharmonic terms, c(x**3 ( c(x**3*exp(-dafac*x**2), etc.

LCDA

lcda [false]

Use the anharmonic factor damping, see also DAFAC.

M4 Options (start immediately on each line of M4.OPT, unlike for S4.OPT)

STRING	OPTION=default value (actual specified on next line)

AD    	AD=.FALSE.

The anharmonic dipole derivatives considered

GEOMETRIES 	GEO=.FALSE.

Geometry correction calculated

LFD   	LFD=.TRUE.

Dipole derivative from FILE.TEN

LTT   	LTTT=.FALSE.

Dipole derivative from FILE.TTT

VCD		LVCD=.TRUE.

Read VCD (from CADPAC)

INS   	LINS=.FALSE.

Inelastic neutron scattering

WRQ      	WRQ=.FALSE.

Extended output

RAMAN      	RAMAN=.FALSE.

Calculate Raman intensities

LCO   	LCORE=.TRUE.

In core spectra calculation

WRONLY     	WRONLY=.FALSE.

Write states, do not calculate spectra

TEMP   	temp=298K

temperature, for case with many ground states

INERTIA    	INERTIA=.FALSE.

IIN1=0      IIN2=0

Calculate rotational constants, mode limits on another line

RES   	LRESTART=.FALSE.

Restart disk-based calculation

GROUND	Ground state definition on the next line:

NGROUND, (IGROUND(i),i=1…NGROUND), by default, NGROUND=1 and IGROUND(1)=0, which means that the lowest-energy state will be taken

N1N2		N1=0, N2=32000

Lower-Upper mode limits

ACU	ACUT=1.0

Expansion cutoff

FGEO 		FGEO=100000 (cm-1)

FGEO limit for geometry calculation

ELIMIT	ELIMIT=999999.9 (cm-1)

Energy limit

Files

| name | type | made in |  |
| --- | --- | --- | --- |
| nA.SCR | bin | dohim | VCI Hamiltonian |
| CFI.SCR | bin |  | block VCI wavefunctions |
| CQCUB.SCR | bin | docqi | cubic constants in normal modes, all |
| CQQ.SCR.TXT | text | docqi | cubic constants in normal modes, (>TOL3) |
| D42.SCR.TXT | text | loadcd | all normal mode quartic constants |
| D42Q.SCR | bin |  | all normal mode quartic constants |
| DIPOLE.TXT.SCR | text |  | property derivatives for averaging |
| DQQ.SCR.TXT | text | dodqi | “IIJK” normal mode quartic constants > ACO |
| EEE.SCR | bin | m4 | block eigenvalues (VCI energies) |
| EEO.SCR | bin | dohbig | all eigenvalues (VCI energies) |
| EIGEN.SCR | bin |  | all VCI wavefunctions |
| FILE.36.OUT | text | INPUT | input for two and three quartic constants, otherwise equivalent to G.OUT |
| FILE.FC | text | INPUT/OUTPUT | harmonic force field |
| FILE.TEN | text | INPUT/OUTPUT | atomic polar and axial tensors |
| FILE.X | text | INPUT/OUTPUT | Cartesian coordinates |
| FS4.INP | text | harmonic | S-matrix |
| G.OUT | text | INPUT | standard input |
| M4.OUT | text | m4 OUTPUT | output with spectral part |
| M4.TAB | text | m4 | anharmonic IR and VCD spectrum |
| M4ROA.TAB | text | m4 | anharmonic Raman and ROA spectrum |
| M4.runwatch | text | m4 | progress of m4 calculation |
| P.FC | text | harmonic | projected Hessian |
| SCR.33 | text | readg98 | cubic constants cijk, i=1,N; j=1,N;k=1,N ¦diijk¦(YLIM |
| SCR.44 | text | readg98 | quartic constants diijk, i=1,N; j=1,N;k=1,N ¦diijk¦(XLIM |
| SCR.36 | text | readg9836 | two-atomic quartic constants, > XLIM |
| SCR.37 | text | readg9836 | three-atomic quartic constants, > XLIM |
| S4.OPT | text | INPUT | standard input with options |
| S4.OUT | text | OUTPUT | main output |
| SMAT.SCR | bin | control | Cartesian-normal mode S-matrix |
| STATES.SCR | bin | ws | VCI states |
| TEN.SCR | bin | readg98.. | ATP and AAT Cartesian derivatives |
| TEN1Q.SCR | bin | readg98i | ATP and AAT normal mode derivatives |
| TEN1Q.TXT.SCR | text | readg98i | ATP and AAT normal mode derivatives |
| TENQ.SCR | bin | readg98i | ATP and AAT normal mode second derivatives |
| TENQ.TXT.SCR | text | readg98i | ATP and AAT normal mode second derivatives |
| TTAQ.SCR | bin | doteni | (,G’,A second normal mode derivatives |
| TTAQ.TXT.SCR | text | doteni | (,G’,A second normal mode derivatives |
| TTQ.SCR | bin | doteni | (,G’,A normal mode derivatives |
| TTQ.TXT.SCR | text | doteni | (,G’,A normal mode derivatives |
| TTT.SCR | bin | readg98 | ( Cartesian derivatives |
| TTTQ.SCR | bin | doteni | ( normal mode derivatives |
| ZIM.SCR | bin | harmonic | atomic masses |

Example:Water molecule absorption spectrum, Cartesian FC

1) optimize geometry

Gaussian input-optimization “opt.inp”

#hf/6-31G opt

h2o

0 1

o  0.0 -0.3 0.0

h  0.8  0.1 0.0

h -0.8  0.1 0.0

2) by “ggopt” get optimized geometry S-orientation for symmetry,

(evetually symmetrize manually FILE.X)

3) make file G.TXT:

%chk=1.chk

$hf/6-31G freq

4) make PMZ.PAR (option file to pmz):

STEP

0.05

IDIF

2

IC

0

END

5) run “pmz”, eventually check FILE.INP

6) get gaussian outputs (“g03 FILE.INP G.OUT”)

7) make a)S.OPT

ENA3

t

SYMMETRY

C2V

VSCF

t

PHASE

t

ENA2

t

END

b)M4.OPT

RAMAN

f

LTT

f

AD

t

GEOMETRIES

t

FGEO

1000.0

END

c)SYM.OPT

1

1

2

8) run “s4”

get the spectra, e.g. “tabprnf M4.TAB 1 4301 100 4400 L 298 10”

Example:Water molecule absorption spectrum, Cartesian FC

9) perform harmonic frequency calculation “harm.out”,

use new1, new2, new4 to make F.INP

10) make PMZ.PAR (option file to pmz):

STEP

0.05

IDIF

2

IC

1

NMD

3

1

2

3

END

11) run “pmz”, eventually check FILE.INP

12) get gaussian outputs (“g03 FILE.INP G.OUT”)

13) make a)S.OPT

ENA3

t

SYMMETRY

C2V

VSCF

t

PHASE

t

ENA2

t

NORMAL MODES

t

NMDI

3 9 8 7

END

b)M4.OPT

RAMAN

f

LTT

f

AD

t

GEOMETRIES

t

FGEO

1000.0

END

c)SYM.OPT

1

1

2

14) run “s4”

get the spectra, e.g. “tabprnf M4.TAB 1 4301 100 4400 L 298 10”